## Slide 1: ENSC 450: Assignment 4
Barry Yim byim@sfu.ca
Cheng Jie (Jadan) Ou jou@sfu.ca
Bonnie Ha bha20@sfu.ca

## Slide 2: Outline
Scope of Presentation:
    Using HSPICE, obtained rise/fall propagation delay and output transition times of simple standard cells
    Conjured liberty file based on timing results
    Optimized liberty file by adding new cells
    PVT conditions for all synthesis and simulations: SS 1.05V 125C
Methodology
Results
Conclusion

## Slide 3: Methodology
Created HSPICE file consisting of NOT, NAND, and NOR cells
    Stimulated rise/fall propagation delay and output transition times of cells
Manually calculated widths, area, and pin capacitance of cells
Constructed worst case conditions liberty file based on simulated and calculated results
Synthesized VHDL code using constructed liberty file
Optimized liberty file by adding new cells
    As a result, decreases max delay of circuit

## Slide 4: Results
Manually calculated widths, areas, and capacitance
 | NOT | NAND | NOR | AND
Wp/Wn Ratio | 4/1 | 4/2 | 8/1 | 4/1
Width of PMOS (nm) | 880 | 880 | 1760 | 880
Width of NMOS (nm) | 220 | 440 | 220 | 220
Area of Cell (μm^2) | 5 | 12 | 18 | 17
Worst Case Capacitance of A | 4 | 4 | 8 | 4
Worst Case Capacitance of B | N/A | 2 | 1 | 1

## Slide 5: Results (2)
As seen from our graph, after the addition of an AND cell, the max delay of the critical path only dropped by a mere 0.02ns. This is due to the fact that:
    Our AND cell was composed of a NAND, followed by a NOT
    The addition of our AND cell to the library was not optimized as we did not increase the transistor widths of the NAND or NOT cell.
    Because the driving strength of cells depend on their transistors' size, there was no significant change in the max delay
    To obtain a significantly lower max delay with the AND cell, we would need to decrease the transistor widths of the NAND cell and increase the transistor widths of the NOT cell.
    By increasing the transistor widths of the NOT cell, we are increasing the output driving strength and thus, decreasing the max delay.

## Slide 6: Conclusion
The purpose of this lab is to create a worst case scenario library with 40% speed up from a minimal standard cell library.
Adding an AND cell, composing of a NAND and NOT cell without adjusting transistor widths, did not make noticeable improvements to the delay.
In order to quickly speed up the delay time, we need to increase the driving power by increasing the widths of the transistors in the last stage of the cell. To optimize the AND cell, we would increase the transistor widths of the NOT cell.
Another way to decrease max delay is to place NOT cells, with large transistor widths, at the input and output nodes of the circuit. This will increase the input and output driving strengths of the circuit.
For example, to optimize the NAND cell, we can place NOT cells at the input and output nodes of the NAND. These NOT cells will have significantly larger transistor widths and thus have significantly larger driving strengths, which will result in much lower max delay times.