## Slide 1: ENSC 450: Register File
Barry Yim byim@sfu.ca
Cheng Jie (Jadan) Ou jou@sfu.ca
Bonnie Ha bha20@sfu.ca

## Slide 2: Outline
Scope of Presentation:
    Designed Register File in VHDL
    Performed automated layout implementation of Register File
    Record timing anaylsis and understand design trade-offs
Description of Register File
Methodology: Front End & Back End Design
Results
Conclusion

## Slide 3: Register File
Contains 32 16-bit registers
Block Diagram: Single Register:
Functions:
    Writes data to specified Data Address location when Write is enabled
    Outputs data from specified Address1 and Address2 registers
VHDL was written by ourselves, with Fabio’s assistance

## Slide 4: Register File (2)
Application:
    Used as temporary storage inside CPU to store values, such as computational, counters, pointers, etc.
Testbench Inputs:
    AddressA, AddressB, AddressIn, DataIn, Clk, Reset, and Write signals as shown below

## Slide 5: Methodology – Front End Design
Using ModelSim, simulate testbench for expected behaviour
Using Synopsys Design Complier, perform logic synthesis
    To evaluate the best possible achievable performance and area/power penality, synthesis design unconstrained (at a high period) and constrained (at the faster possible period)
    Evaluate timing, area, and power results
Optimize Design by selecting reasonable period
Using ModelSim, verify expected behaviour of synthesized netlist

## Slide 6: Synthesis Results
Critical Path: from addressA[1] to outA[0]
    Longest delay is input external delay = 0.80ns
    Input external delay is due to input and output wires parasitic from the clock to the register
    Total data arrival time = 2.60ns
Period (ns) | Frequency(MHz) | Area (um^2) | Data Arrival Time (ns) | MET/VIO | Total Dynamic Power (uW)
3.25 | 308 | 5977.020115 | 2.44 | MET | 1487.3
3.5 | 286 | 5962.656114 | 2.6 | MET | 1367.8
7 | 143 | 5962.390114 | 2.6 | MET | 683.8518
10 | 100 | 5962.390114 | 2.6 | MET | 478.6962
15 | 67 | 5962.390114 | 2.6 | MET | 319.1308
25 | 40 | 5962.390114 | 2.6 | MET | 191.4785

## Slide 7: Optimization
Plotting the results:
        The highest frequency we can run our circuit at without compromising area is at 286MHz
    Additionally, 40Mhz is the lowest frequency we can run our circuit at without violating setup times
    Thus, we will perform Back End Design at 286MHz (period = 3.5ns) and 40Mhz (period = 25ns)

## Slide 8: Methodology – Back End Design
Using Encounter and scripts provided, perform:
    Import Design & Floor Planning
    Placing & Optimization
    Clock Tree Synthesis & Optimization
    Routing & Finishing
Checked session logs for errors and major warnings. Also, checked reports for design violations
Analyzed timing reports and summaries

## Slide 9: Constraints
Using TT transistor characteristics with 045nm technology at 25oC, constrained design with a 3.5ns and 25ns clock period.
Fitted design into a chip with an area of ~8000um2.
Floor plan density = 90%
Period | Max Clock Skew | Max Latency
20ns | 0.625ns | 3.29ns
3.5ns | 0.686ns | 3.28ns

## Slide 10: Back End Design Results
Period 3.5ns:
Since our circuit is a Register File, speed is important. Hence, it would be best to run at 3.5ns for faster arrival time, despite small increase in area and density
Period 25ns:
Stage | Number of Cells | Cell Area μm2 | Density | Data Arrival Time
Post-Synthesis | 3647 |  |  | 2.3439
Placing | 3518 | 5807.844 | 87.66% | 2.65340
Post-Place OPT | 3567 | 5852.798 | 88.34% | 2.61520
CTS | 3682 | 5872.748 | 88.64% | 2.61780
Post-CTS OPT | 3582 | 5874.344 | 88.66% | 2.57260
Routing/Signoff | 3582 | 5874.344 | 88.66% | 2.55380
Finishing | 4667 | 5874.344 | 99.90% | 2.55380
Stage | Number of Cells | Cell Area μm2 | Density | Data Arrival Time
Post-Synthesis | 3647 |  |  | 2.34391
Placing | 3518 | 5807.578 | 87.66% | 2.67560
Postplace OPT | 3527 | 5801.194 | 87.56% | 2.68840
CTS | 3542 | 5821.144 | 87.87% | 2.67830
Post CTS OPT | 3542 | 5826.996 | 87.95% | 2.6266
Routing/Signoff | 3542 | 5826.996 | 87.95% | 2.68661
Finishing | 4880 | 5826.996 | 99.90% | 2.68661

## Slide 11: Back End Design Results (2)
After performing Place & Route, we were happy with our results because we didn’t have any unresolved violations in our circuit.
    Thus, no changes to Floor Plan or constraints were applied.
During optimization steps, trial routing was performed to estimate wire loads and delays
    Buffers were inserted to decrease timing delays

## Slide 12: Conclusion
Chose to conclude with a Register File made with 45nm technology and 3.5ns clock period
    Compared to the 25ns clock period, area is basically the same
    Can run 5% faster than 25ns clock period
At Period=3.5ns, the performance of our device is:
    Area of Standard Cells: 5874.344 μm2
    Cell Utilization: 88.755%
    Core Density (without filler cells): 88.66%
    Unresolved violations and problems: None
    Data Arrival Time: 2.55380 ns